## Slide 1: EnergyPlus 8.2 Getting Started in Command Line

## Slide 2: Installation
On MacOS
  Apply the dmg package at
    http://apps1.eere.energy.gov/buildings/energyplus/register.cfm?goto=eplus
  Or download from my shared link
    https://drive.google.com/file/d/0Bzn8tD_Jzg_qbURvcDY2dkR5anM/view?usp=sharing

## Slide 3: Installation cont’d
After installation, some commands are available:
  EnergyPlus
  EPMacro
  runenergyplus // we use this for CLI testing
Type in terminal to verify
  runenergyplus

## Slide 4: EnergyPlus Dir Hier on Mac
/Application/EnergyPlus-8.x.y/
  ExampleFiles/
    Example *.idf files, describes sample buildings
  WeatherData/
    Example *epw files, describes weathers at some example locations
  Documentation/
  . . .
We use *.idf and *.epw to do the simulations

## Slide 5: Run EnergyPlus
Prepare IDF file and EPW file
  Using WindACAuto.idf to describe building
    Copied from /Applications/EnergyPlus-8-2-7/ExampleFiles/WindACAuto.idf
  Using USA_CA_San.Francisco.Intl.AP.724940_TMY3.epw to describe weather
    Copied from /Applications/EnergyPlus-8-2-7/WeatherData/USA_CA_San.Francisco.Intl.AP.724940_TMY3.epw

## Slide 6: Run EnergyPlus cont’d
Command format
  runenergyplus InputFileName [WeatherFileName]
In this example
  runenergyplus WindACAuto.idf USA_CA_San.Francisco.Intl.AP.724940_TMY3.epw
Generate directory “Output/”

## Slide 7: Output files
Temperature data appears in WindACAuto.csv
  Can be imported into excel (choose comma as delimiter)
And many other files
  .svg – HVAC diagram
  .mtr – raw report meter output
  .err – list of errors and warnings
  And more… (see GettingStarted.pdf, page 14)

## Slide 8: Plot sample from WindACAuto.csv
Chart: 

## Slide 9: IDF files
Describes everything related to the building
  Wall materials and structure
  Exposure to sunlight
  Zone-based-
    Floor plan definition
    Electric equipment, HVAC
    Occupancy
Output specification

## Slide 10: EPW (EnergyPlus Weather) files
Historical weather data
Used for provide environmental weather conditions for simulation

## Slide 11: Preprocessor and Postprocessor
EngeryPlus usually works as simulation engine for Sketchup and Openstudio
Sketchup can be used to design and construct the building
Openstudio can be utilized to set the conditions inside the building and generate reports.

## Slide 12: Sketchup
The file type of Sketchup are .skb and .osm, can open Energyplus .idf file and Openstudio .osm file.
Import Openstudio file:
Import EngergyPlus file:

## Slide 13: An example in Sketchup
A house with roof, wall, window and shades:

## Slide 14: Run EnergyPlus in Sketchup
Choose this option will run EnergyPlus in the Sketchup
Choose the .epw weather file

## Slide 15: Generate Report

## Slide 16: Openstudio
The file type of Openstudio is .osm file.
Openstudio Interface
First, need to input the weather .epw file and Design days .ddy file

## Slide 17: Setting for each thermal zone

## Slide 18: Setting for each thermal zone
The setting includes:
Thermal Zones
Space Type
Schedule
Outdoor Air
People
Lights
Electric Equipment
Gas Equipment
Water Use Equipment
Surfaces
Etc.

## Slide 19: Setting for the simulation
Choose the convergence limits and convergence algorithm in the setting.

## Slide 20: Run the model

## Slide 21: Result
Use this to get more results

## Slide 22: Result
Use Flood Plot or Line Plot:

## Slide 23
Flood Plot:

## Slide 24
Line Plot: