## Slide 1: Sensitivity Analysis in Building Energy Simulation using Sparse Regression

## Slide 2: Case setup
10 floors
  Identical floorplan for each floor
90 thermal zones (rooms)
1020 variables
  740 physical variables
  12 ground temperatures
  270 user behavior variables

## Slide 3: Variation of variables
Ground temperature ~N(mean, 0.2 ℃)
Thickness ~N(mean, 5%)
Conductivity ~(mean, 20%)
Density ~N(mean, 5%)
Specific Heat ~N(mean, 20%)
Thermal Absorptance ~N(mean, 20%)
Solar Absorptance ~N(mean, 20%)
Visible Absorptance ~N(mean, 20%)
Thermal Resistance ~N(mean, 20%)
Equipment power per area ~U(mean, ±40%)
Area per person ~U(mean, ±40%)

## Slide 4: Simulation flow
Randomly generate N samples using Latin hypercube sampling method, and form an N*K matrix (K: #variable)
Perform N EnergyPlus simulations, and get N results (e.g., annual heating energy consumption)
Do sensitivity analysis
  Full linear regression
  OMP (Orthogonal Matching Pursuit)
  LASSO (Least Absolute Shrinkage and Selection Operator)

## Slide 5: Cross-validation for OMP
Optimal L0 norm for OMP: 260 (for 2000 samples)
Chart: 
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300
 | 0.090571 | 0.069941 | 0.053202 | 0.042717 | 0.038226 | 0.034746 | 0.031769 | 0.028166 | 0.026237 | 0.025019 | 0.024214 | 0.024135 | 0.024022 | 0.02391 | 0.023802 | 0.023746 | 0.023677 | 0.023668 | 0.023596 | 0.023629 | 0.02341 | 0.023229 | 0.023245 | 0.023276 | 0.023224 | 0.023213 | 0.023311 | 0.023503 | 0.023504 | 0.02361

## Slide 6: Cross-validation for LASSO
Optimal L1 norm for LASSO: 9.6 (for 2000 samples)
Chart: L1 norm
| 6 | 6.1 | 6.2 | 6.3 | 6.4 | 6.5 | 6.6 | 6.7 | 6.8 | 6.9 | 7 | 7.1 | 7.2 | 7.3 | 7.4 | 7.5 | 7.6 | 7.7 | 7.8 | 7.9 | 8 | 8.1 | 8.1999999999999993 | 8.3000000000000007 | 8.4 | 8.5 | 8.6 | 8.6999999999999993 | 8.8000000000000007 | 8.9 | 9 | 9.1 | 9.1999999999999993 | 9.3000000000000007 | 9.4 | 9.5 | 9.6 | 9.6999999999999993 | 9.8000000000000007 | 9.9 | 10 | 10.1 | 10.199999999999999 | 10.3
 | 0.032895 | 0.032223 | 0.031579 | 0.030965 | 0.030376 | 0.02981 | 0.029265 | 0.028747 | 0.028249 | 0.027785 | 0.027349 | 0.026936 | 0.026545 | 0.026174 | 0.025827 | 0.025499 | 0.025191 | 0.024906 | 0.024638 | 0.024384 | 0.024147 | 0.023926 | 0.023724 | 0.023538 | 0.023363 | 0.023195 | 0.023037 | 0.022889 | 0.022756 | 0.022642 | 0.022549 | 0.022469 | 0.022404 | 0.022349 | 0.022305 | 0.022279 | 0.022269 | 0.02227 | 0.022287 | 0.022321 | 0.022369 | 0.022428 | 0.022499 | 0.022579

## Slide 7: #sample & modeling error
Chart: #sample
| 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500 | 2000 | 2500 | 3000 | 3500 | 4000 | 4500 | 5000 | 6000 | 7000 | 8000 | 9000
Linear Regression | 0.045985 | 0.040165 | 0.035506 | 0.031712 | 0.025417 | 0.022536 | 0.021862 | 0.02107 | 0.020567 | 0.02014 | 0.019834 | 0.019466 | 0.01905 | 0.01853 | 0.018161
OMP | 0.039321 | 0.034342 | 0.031208 | 0.027536 | 0.02515 | 0.025169 | 0.023892 | 0.02368 | 0.023345 | 0.023746 | 0.02271 | 0.020837 | 0.020067 | 0.019258 | 0.019089 | 0.018679
LASSO | 0.032075 | 0.030079 | 0.026552 | 0.025664 | 0.024614 | 0.024014 | 0.023195 | 0.023131 | 0.022398 | 0.021635 | 0.021306 | 0.019956 | 0.019385 | 0.019193 | 0.018856 | 0.018591

## Slide 8: Sensitivities of factors
Chart: Sorted factor index

## Slide 9: Most significant factors
Factor | Regression coefficient
Conductivity of floor | ~0.18
Ground temperature | 0.04~0.16
Equipment power | 0.03~0.16
Thickness of floor | 0.04~0.05
Thermal resistance of wall | ~0.025
Thermal absorptance of wall | 0.012~0.015
Solar absorptance of wall | ~0.011
Area per person | ~0.01