## Slide 1: EnergyPlus 8.2 Getting Started in Command Line
Hengyang Zhao

## Slide 2: Installation
On MacOS
  Apply the dmg package at
    http://apps1.eere.energy.gov/buildings/energyplus/register.cfm?goto=eplus
  Or download from my shared link
    https://drive.google.com/file/d/0Bzn8tD_Jzg_qbURvcDY2dkR5anM/view?usp=sharing

## Slide 3: Installation cont’d
After installation, some commands are available:
  EnergyPlus
  EPMacro
  runenergyplus // we use this for CLI testing
Type in terminal to verify
  runenergyplus

## Slide 4: EnergyPlus Dir Hier on Mac
/Application/EnergyPlus-8.x.y/
  ExampleFiles/
    Example *.idf files, describes sample buildings
  WeatherData/
    Example *epw files, describes weathers at some example locations
  Documentation/
  . . .
We use *.idf and *.epw to do the simulations

## Slide 5: Run EnergyPlus
Prepare IDF file and EPW file
  Using WindACAuto.idf to describe building
    Copied from /Applications/EnergyPlus-8-2-7/ExampleFiles/WindACAuto.idf
  Using USA_CA_San.Francisco.Intl.AP.724940_TMY3.epw to describe weather
    Copied from /Applications/EnergyPlus-8-2-7/WeatherData/USA_CA_San.Francisco.Intl.AP.724940_TMY3.epw

## Slide 6: Run EnergyPlus cont’d
Command format
  runenergyplus InputFileName [WeatherFileName]
In this example
  runenergyplus WindACAuto.idf USA_CA_San.Francisco.Intl.AP.724940_TMY3.epw
Generate directory “Output/”

## Slide 7: Output files
Temperature data appears in WindACAuto.csv
  Can be imported into excel (choose comma as delimiter)
And many other files
  .svg – HVAC diagram
  .mtr – raw report meter output
  .err – list of errors and warnings
  And more… (see GettingStarted.pdf, page 14)

## Slide 8: Plot sample from WindACAuto.csv
Chart: 

## Slide 9: IDF files
Describes everything related to the building
  Wall materials and structure
  Exposure to sunlight
  Zone-based-
    Floor plan definition
    Electric equipment, HVAC
    Occupancy
Output specification

## Slide 10: EPW (EnergyPlus Weather) files
Historical weather data
Used for provide environmental weather conditions for simulation